## Slide 1
Discrimination of Objects Mounted on
Optical Bench Using Ultrasonic Sensing
and Machine Learning
Presented by:
[Romana Rashid - 1428733] · [Mithila Maruti Prabhu- 1567111]
Supervisor:
Dr. Andreas Pech
Machine Learning Project | Winter Semester 2025–2026
4
Material Classes
3
ML Models
2
Recording Sessions
26
Distances (5–30 cm)
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 2
Project Overview
Identifying material types by analysing reflected ultrasound signals
1
Raw Signals
ADC recordings from ultrasound sensor
→
2
Feature Extraction
15 time + frequency domain features
→
3
ML Models
RF · SVM · KNN
→
4
Day 1 Training
80/20 stratified split
→
5
Day 2 Evaluation
Cross-session test
→
6
Results
Accuracy, F1, drift
Objective
Classify 4 materials from ultrasound reflections
Train ML models on time & frequency features
Evaluate cross-session generalisation
Approach
Collect ADC signals at 5–30 cm (26 positions)
Extract 15 statistical & spectral features
Train RF, SVM, KNN — evaluate on Day 2 data
Motivation
Non-invasive material ID for robotics & logistics
Ultrasound: cost-effective, works in low-visibility
Benchmark temporal drift on model reliability
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 3
Data Collection & Setup
Two recording sessions — 4 material classes at 26 distance positions
4
Material Classes
26
Distances (5–30 cm)
2
Recording Sessions
~2600
Measurements / Session
Laptop
Smooth flat metallic-plastic surface, moderate reflectivity
PB w/ Foam
Dampened box — foam absorbs partial signal energy
PB w/o Foam
Hollow plastic shell — stronger internal echoes
Steel
High-density smooth reflector, strongest signal amplitude
Day 1 — Training Session
Used for training all ML models (80/20 stratified split)
Data: /data/raw/ — 26 distances × 4 classes
Day 2 — Evaluation Session
Recorded independently — tests temporal drift & robustness
Data: /data/raw_day2/ — same structure as Day 1
Signal Format: Each .txt file contains multiple ADC rows. Header encodes sample rate (32768 Hz), buffer size, sensitivity (84), measurements, frequency (512 Hz). Each row provides tab-separated ADC values forming a full waveform.
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 4
Feature Engineering
15 hand-crafted features per measurement from time & frequency domain
⏱ Time-Domain Features (10)
Feature | Description
mean | Average signal amplitude
std | Amplitude variability
max / min | Peak positive/negative values
ptp | Peak-to-peak range
rms | Root mean square energy
energy | Total signal power (∑ x²)
abs_mean | Mean of absolute values
argmax / argmin | Sample indices of peaks
📈 Frequency-Domain Features (5)
Feature | Description
fft_mean | Average spectral magnitude
fft_std | Frequency content spread
fft_max | Dominant frequency amplitude
fft_peak_bin | Index of dominant frequency bin
fft_energy | Total spectral energy (∑¦X¦²)
Distance (cm) is included as an explicit numeric feature
FFT features computed via scipy.fft.rfft on the raw ADC signal
Normalisation via StandardScaler inside SVM & KNN pipelines
Total dataset: ~2600 rows × 16 columns (15 features + distance)
Two feature sets: Full range (26 distances) and 4-distance subset (10, 15, 20, 25 cm)
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 5
Machine Learning Models
Three classifiers compared — trained on Day 1, tested on Day 2
Random Forest
Hyperparameters
n_estimators = 500
max_depth = None
min_samples_split = 2
random_state = 42
✓ Strengths
Handles non-linear boundaries naturally
Robust to outliers
Provides feature importance
⚠ Limitations
Slower inference for large forests
Memory-intensive
SVM (RBF Kernel)
Hyperparameters
kernel = RBF
C = 10
gamma = scale
StandardScaler pre-processing
✓ Strengths
Effective in high-dimensional spaces
Strong generalisation (kernel trick)
Works well with clear margins
⚠ Limitations
Slow training on large datasets
No native probability output
K-Nearest Neighbours
Hyperparameters
n_neighbors = 7
weights = distance
StandardScaler pre-processing
✓ Strengths
Non-parametric, no training phase
Naturally multi-class
Interpretable predictions
⚠ Limitations
Slow at inference (all training distances)
Sensitive to feature scaling
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 6
Model Performance — Overall Accuracy
Day 1 training vs Day 2 cross-session evaluation
RF dominates Day 1 with 82.4% — large advantage over SVM/KNN
All models degrade heavily on Day 2 full range (~35%) — temporal drift is significant
4-distance RF model recovers to 51.8% by limiting to well-characterised distances
SVM and KNN show less benefit from 4-distance restriction
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 7
Accuracy vs. Distance — Full Range
How model performance varies across the 26 measurement distances on Day 2 (5–30 cm)
RF maintains highest accuracy at most distances on Day 2
Performance is highly variable and distance-dependent for all models
Middle range (15–20 cm) generally shows better classification
Short distances (≤10 cm) and very long distances (≥25 cm) tend to be harder
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 8
4-Distance Subset Analysis
Restricted training at 10, 15, 20, 25 cm — Full-Range vs 4-dist model comparison on Day 2
RF 4-dist model: 51.8% on 4-dist Day 2 — significant +16 pp gain over full-range
Restricting distances reduces noise from outlier positions
SVM/KNN do not benefit as much — limited feature separability
Distance-selective training is a viable strategy to mitigate temporal drift
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 9
Confusion Matrices — Day 2 Evaluation
Which classes are misclassified and why
Full Range — Day 2
4-Distance Model — Day 2
Steel best classified by RF 4-dist (70%) — high acoustic impedance contrast
PB w/o foam most confused — hollow echo varies with distance
4-dist RF shows clear diagonal dominance vs diffuse full-range patterns
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 10
Temporal Drift Analysis
Signal characteristics shift between recording sessions
Systematic shift in signal statistics between Day 1 and Day 2 due to environmental changes
RF drops from 82.4% (Day 1) to 35.3% (Day 2 full range) — a loss of ~47 pp
Mitigation: restrict training distances, domain adaptation, or periodic re-training
4-dist RF partially recovers to 51.8%, confirming curated data helps cross-session robustness
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 11
F1-Score Heatmap by Class
Per-class performance reveals which materials are hardest to identify (Day 2)
RF 4-dist achieves F1=0.76 for Steel — highest score across all configurations
PB w/o foam is consistently the hardest class (F1 as low as 0.11 in 4-dist SVM/KNN)
Steel is most reliably classified; foam-padded plastic box is hardest across all models
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 12
Per-Class Precision, Recall & F1
Detailed breakdown for all 6 model configurations on Day 2 ★ NOT IN ORIGINAL PRESENTATION
RF 4-dist achieves best Steel precision (82%) and recall (70%) — strong class-specific detection
PB w/o foam suffers low recall in 4-dist models (SVM: 8%, KNN: 8%) — many missed detections
PB w/ foam: balanced precision/recall in full-range models; recall drops sharply in 4-dist SVM/KNN
Full-range models show flatter, more balanced profiles — no single class dominates
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 13
Model Confidence Analysis
Correct vs. Incorrect prediction confidence — Day 2 full range ★ NOT IN ORIGINAL PRESENTATION
RF: correct predictions (mean=0.56) only slightly more confident than incorrect (mean=0.51)
KNN: correct predictions (mean=0.65) show better separation from incorrect (mean=0.56)
Models are often near-equally confident in wrong predictions — limited self-awareness of errors
KNN confidence by class: Laptop correct predictions hit 0.80 mean — most distinctive signal class
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 14
Per-File Classification (Majority Vote)
Aggregating per-measurement votes per recording — Day 2 full range ★ NOT IN ORIGINAL PRESENTATION
Majority vote improves RF: 35.3% → 39.4%; SVM: 31.3% → 32.7%; KNN: 32.3% → 33.7%
Aggregating predictions per file provides marginal but consistent accuracy gains
SVM achieves 54% per-file accuracy on PB w/ foam — best single-class result in majority vote
Steel and PB w/o foam remain the hardest classes even with majority voting aggregation
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 15
Results Summary
Comprehensive comparison of all model–evaluation configurations
Configuration | Model | Accuracy | Notes
Day 1 (train=test) | Random Forest | 82.4% | Strong in-session performance
Day 1 (train=test) | SVM | 64.8% | Competitive but lower than RF
Day 1 (train=test) | KNN | 65.7% | Similar to SVM
Day 2 Full (full model) | Random Forest | 35.3% | Significant drift drop
Day 2 Full (full model) | SVM | 31.3% | Near-chance performance
Day 2 Full (full model) | KNN | 32.3% | Near-chance performance
Day 2 4-dist (full model) | Random Forest | 37.6% | Slight improvement
Day 2 4-dist (4d model) | Random Forest | 51.8% ✓ | Best cross-session result
Day 2 4-dist (4d model) | SVM | 30.6% | No improvement with 4d model
Day 2 4-dist (4d model) | KNN | 35.3% | Minor improvement
Object Boundary Network (OBN) — Material Classification via Ultrasound

## Slide 16
Conclusions & Future Work
82.4%
Best Day 1
Accuracy (RF)
51.8%
Best Day 2
Accuracy (RF 4d)
4
Materials
Classified
15
Features
Extracted
Key Findings
Random Forest (82.4%) outperforms SVM (64.8%) and KNN (65.7%) on Day 1
Cross-session performance degrades substantially — temporal drift is a critical challenge
4-distance restricted RF model achieves 51.8% — best Day 2 result (+16 pp over full-range RF)
Steel is the easiest material to classify; foam-padded plastic box is the hardest
Distance is an important feature — models trained on near-field distances generalise better
SVM & KNN show limited benefit from 4-distance restriction strategy
Future Work
Apply domain adaptation / transfer learning for cross-session robustness
Explore deep learning (1D CNN, LSTM) directly on raw ADC signals
Automated distance selection to find optimal measurement windows
Expand material classes — wood, glass, composite materials
Real-time classification on embedded hardware (Raspberry Pi / Arduino)
Collect additional sessions to build a longitudinal drift model
Object Boundary Network (OBN) — Material Classification via Ultrasound